## Slide 1: Meeting 10
Tuesday 27/03/2018

## Slide 2: Agenda
LES
  Wind turbine and output
  LES output
Turbulence intensity
Wind profile
  Inflow profile
  Comparison WMR & LES wind speeds
Horizontal profile
Next steps
Midterm meeting

## Slide 3: 1a. LES Wind turbine
Notes: DTU10MW turbine scaled (red) to WMR wind turbine (black): matches very close

## Slide 4: 1b. LES output (Case 3)
Notes: 1st figure: Vhub = wind velocity at hub height, 1R upstream of 1st wind turbine
Black power curve: power derived from Vhub and power curve
The electrical power (Pelec) is exceeding Prated, up to 7MW and for long time periods These points in time are indicated in orange (both in the power curve as for Vhub)
Reasons why the black power curve is lower than the blue one: induction, shear, steady state power curve
Mean ( Pelec / Pfrom power curve)=1,844

## Slide 5: 1b. LES output(Case 3)
Notes: Black curves: interpolated values making use of Vhub and pitch/thrust curve
Orange: when Pelec exceeds Prated
Pitch behaves as expected
Thrust is too high in LES simulations! Because of intertia you gain a bit extra thrust, but not this much

## Slide 6: 1b. LES output(Case 3)

## Slide 7: 2. Turbulence Intensity BEACon (Case 3)
Nacelle anemometer and power production of wind turbine A01
The TI based on the nacelle anemometer over this 10-minute period is 11.7%.
The TI based on the wind speed derived from the power data is only 4.6%.
(Calculations by Nicolai)
Notes: Power curve: “averaged” value, does not react instantaneously  lower TI

## Slide 8: 2. Turbulence Intensity LES (Case 3)
TI based on 10-min averages
Turbulence is imposed in planes at 3,95D upstream of the first turbine
TI calculated at different positions downstream
Notes: Cross-strea planes for LES are only available up to 1D upstream (see also next slide)
Purple line: LES turbulence, also averaged in space
TI in LES is created with body forces
Matches TI at hub height quite well with the BEACon TI
Could be tuned up a little bit in the LES situations, but will not make a big difference

## Slide 9: 3a. Inflow wind profile
Inflow profile BEACon: spatial averaged velocity (cross-stream plane)
Inflow profile LES
  Yellow: data only from one line
  Yellow-green: spatial averaged velocity (cross-stream plane)
Notes: Cross-stream planes for LES are only available up to 1D upstream

## Slide 10: 3a. Inflow wind profile: BEACon
Difference Wind speed at 100m and 106m
U0 is actually at 100m –> gives already too low input velocity for LES
Spatial averaged inflow wind profile (Case 3)
Notes: 9,5m/s is used as inflow velocity at hub height (106m), but is actually at 100m  Inflow wind speed of LES simulations should be increased

## Slide 11: 3a. Inflow wind profile: WMR
Spatial averaged inflow wind profile (Case 1)
Notes: 11,8m/s is used as inflow velocity at hub height (106m), but is actually at 100m  Inflow wind speed of LES simulations should be increased

## Slide 12: 3a. Comparison WMR & LES wind profiles (Case 3)
Inflow profiles at different upstream positions
Where do we want to match them?
Notes: Different ways of calculating LES time average
  Ensemble (as shown previous meeting)
  Total mean: mean of all values (after transien)
The difference between the LES and BEACon profiles is +- constant for different locations upstream (due to wind speed at 100m used instead of 106m)
For -1D upstream also data of cross-stream plane available: also spatial averaging

## Slide 13: 3a. Comparison WMR & LES wind profiles (Case 1)
Inflow profiles at different upstream positions
Where do we want to match them?

## Slide 14: 3a. Inflow wind profile
Inflow profile BEACon: spatial averaged velocity (cross-stream plane)
Inflow profile LES: data only from one point
Blue: 106m height (hub) Pink: 100m height
Notes: Wind speeds at 100m
Wind speeds at 106m
Upstream locations: -5D, -4D, -3D, -2D and -D

## Slide 15: 3b. Comparison WMR & LES wind speeds
Wind speed at 100m and 106m: BEACon and LES
Case 3
Notes: The LES wind speeds far upstream are too low As a comparison they are scaled with the log law in the next slide

## Slide 16: 3b. Comparison WMR & LES wind speeds
Wind speed at 100m and 106m: BEACon & LES with scaling (log(106)/log(100))
Case 3
Notes: - The scaling is not used to scale all LES results! This is just an indication that the inflow wind speed for the LES data should be increased

## Slide 17: 3b. Comparison WMR & LES wind speeds
Wind speed at 100m and 106m: BEACon and LES
Case 1

## Slide 18
3b. Comparison WMR & LES wind speeds
Wind speed at 100m and 106m: BEACon & LES with scaling (log(106)/log(100))
Case 1

## Slide 19
3b. Comparison WMR & LES wind speeds + simple model induction
A simple model of the wind turbine induction zone derived from numerical simulations – N.Troldborg et al.

## Slide 20
3b. Comparison WMR & LES wind speeds + simple model induction (Case 3)
Notes: Normalized with Uo=9,5 m/s
The induction model

## Slide 21
3b. Comparison WMR & LES wind speeds + simple model induction (Case 3)
Notes: Non-normalized for Case 3

## Slide 22
3b. Comparison WMR & LES wind speeds + simple model induction (Case 1)
Notes: Normalized with Uo=9,5 m/s
The induction model

## Slide 23: 4. Horizontal profile
WMR: at 100m height
LES
  at 100,24 m and 107,53 m height
  Spatial averaged at 100 m height

## Slide 24: 4. Horizontal profile
Notes: At different downstream positions

## Slide 25: 4. Horizontal profile
Notes: The spatial averaging has a very limited effect: do not worry about this
Blue(/black) and red curve should be compared
BEACon profile is very smooth
Suggestion: make error bar around mean WMR (now only mean plotted)

## Slide 26
Notes: Compare black and red curves

## Slide 27: Next steps
New LES simulations
  Turbulence Intensity
  Inflow wind speed
Power spectrum (Nicolai)
Superposition of LES results
  Comparison wind field 1WT and wind field 3WT
Notes: Detect (to seperate questions/conclusions):
  Super position
  Single wake induction
Focus on horizontal plane (at 100m)
  Mean
  Cross-correlation in time for each point (1WT // 3WT)
  Look which superpostion method (linear, quadratic, max deficit) is closest to the LES results. Or another method/scaling used?

## Slide 28: Midterm meeting
Monday 16/04, 9:30-10:30
Calendar invitation
15-20 min presentation + questions
Draft report
Next meeting? (Tuesday 10/04 at 14:00)
Notes: During midterm meeting not the time to discuss as much in detail as we can do during the normal meetings
Midterm: everything that has been done + what the big next steps are (planning)
Midterm draft report: the people who don’t know until now what I’ve been doing, should have an understanding of what the thesis is about