## Slide 1: Meeting 8
Tuesday 27/02/2018

## Slide 2: Agenda
Park model: test case
Sensitivity study
LES data & BEACon data
Calibration
Next steps

## Slide 3: 1. Park model: test case

## Slide 4: Sensitivity study
Parameter | 
U0 | 10 m/s
Wake coefficient k | Variable
Wind turbine distance | Variable
Superposition method | Quadratic
Correction factor | True
Wake reflection | False/True
CT curve | WMR
Wind speed deficit at 3rd wind turbine

## Slide 5: Sensitivity study
Parameter | 
U0 | 10 m/s
Wake coefficient k | 0,04
Wind turbine distance | 7*D
Superposition method | Variable
Correction factor | False/True
Wake reflection | False/True
CT curve | WMR

## Slide 6: Sensitivity study
Parameter | 
U0 | 10 m/s
Wake coefficient k | 0,04
Wind turbine distance | 7*D
Superposition method | Variable
Correction factor | True
Wake reflection | False/True
CT curve | WMR

## Slide 7: Sensitivity study
Parameter | 
U0 | Variable
Wake coefficient k | 0,04
Wind turbine distance | 7*D
Superposition method | Quadratic
Correction factor | True
Wake reflection | True
CT curve | Variable

## Slide 8: Sensitivity study
Parameter | 
U0 | 10
Wake coefficient k | Variable
Wind turbine distance | 7*D
Superposition method | Quadratic
Correction factor | True
Wake reflection | True
CT curve | Variable

## Slide 9: Sensitivity study
Parameter | Park 1 | Park 2
U0 | 10 | 10
Wake coefficient k | 0,04 | 0,06
Wind turbine distance | 7*D | 7*D
Superposition method | Quadratic | Linear
Correction factor | True | False
Wake reflection | True | False
CT curve | WMR | WMR

## Slide 10: LES data
Calculation of mean
  Tend= 1436,1 s ≈ 23,93 min
  deltaT=0,1058 s
  Neglect first 300 seconds due to transient
    It takes +- 300 s to reach the third wind turbine (U=11,8 m/s)
  Calculate moving mean
    Window = 600 s, only full windows
    Umean = mean of moving mean
    Ustd = std of moving mean

## Slide 11: BEACon data
Rotor averaged wind speed
  Change position of rotor behind second wind turbine?
No data for lower part rotor
  Averaged wind speed would decrease

## Slide 12: BEACon + LES data

## Slide 13: Calibration
Parameter | 
U0 | 11,8
Wake coefficient k | Variable
Superposition method | Quadratic
Correction factor | True
Wake reflection | True
CT curve | WMR

## Slide 14: Calibration
Parameter | 
U0 | 11,8
Wake coefficient k | Variable
Superposition method | Quadratic
Correction factor | True
Wake reflection | True
CT curve | WMR

## Slide 15: Next steps
Calibration
WAsP results